## Slide 1: Device Model Summary Model ID = dtmi:com:Microchip:WFI32_Curiosity_WM;1 File Name = wfi32_curiosity_wm-1.json
Type | Name | Schema | Example JSON Message/Format
Telemetry | WFI32Curiosity_temperature | double | {“WFI32Curiosity_temperature”:26.8175}
Telemetry | ALT2_altitude | double | {“ALT2_altitude”:1054.382}
Telemetry | ALT2_pressure | double | {“ALT2_pressure”:34.69}
Telemetry | ALT2_temperature | double | {“ALT2_temperature”:23.261}
Telemetry | PHT_humidity | double | {“PHT_humidity”:51.731}
Telemetry | PHT_pressure | double | {“PHT_pressure”:27.5093}
Telemetry | PHT_temperature | double | {“PHT_temperature”:21.336}
Telemetry | TEMPHUM14_humidity | double | {“TEMPHUM14_humidity”:62.59}
Telemetry | TEMPHUM14_temperature | double | {“TEMPHUM14_temperature”:18.44}
Telemetry | ULP_pressure | double | {“ULP_pressure”:45.12}
Telemetry | ULP_temperature | double | {“ULP_temperature”:20.809}
Telemetry | VAV_pressure | double | {“VAV_pressure”:66.377}
Telemetry | VAV_temperature | double | {“VAV_temperature”:27.648}
Telemetry | button_event | Object | {“button_event”:{“button_name”:“SW1”, “press_count”:7}}

## Slide 2: Device Model Summary Model ID = dtmi:com:Microchip:WFI32_Curiosity_WM;1 File Name = wfi32_curiosity_wm-1.json
Type | Name | Schema | Example JSON Message/Format
Property (Read Only) | led_g | LedState | {“led_g”:1}
Property (Read Only) | led_r | LedState | {“led_r”:2}
Property (Writable) | telemetryInterval | integer | {“telemetryInterval”:{“ac”:200,“av”:55, “ad”:“OK”,“value”:10}}
Command (Request) | reboot | Object | {“payload”:{“delay”:“PT5S”}}
Command (Response) | reboot | Object | {“response”:{“status”:“success”,“delay”:5}}
Command (Request) | sendMsg | Object | {“payload”:{“sendMsgString”:“Hello World!!!”}}
Command (Response) | sendMsg | Object | {“response”:{“status”:“received”}}